## Slide 1: BudWatch Temperature and Humidity Monitoring System for Cannabis Storage Boxes
Jay Urscheler, Feb 15, 2025
George Brown College Capstone COMP3099
Project for Summerleaf Saugeen, Sauble Beach

## Slide 2: Project Overview
Objective: Develop a system to monitor temperature and humidity in cannabis storage boxes.
Purpose: Ensure optimal storage conditions for Summerleaf Saugeen’s products.
Scope:
  Design and build a sensor-based monitoring system.
  Collect, store, and visualize data.
  Provide a user-friendly solution for the business.

## Slide 3: Project background
Local cannabis store (Summerleaf Saugeen) has concerns on humidity in storage room, where cannabis products are stored in storage boxes.
Cannabis products should be stored between 15-21°C and 55-62% humidity.
Store owner would like to be able to monitor the temperature of each storage container and ideally get notified if the temperature or humidity falls outside of the above-mentioned threshold.

## Slide 4: Project Plan
Phases:
  Research and Requirements Gathering
  System Design
  Prototyping
  Implementation
  Data Management and Visualization
  Testing and Validation
  Deployment and Maintenance

## Slide 5: Research and Requirements
Identified business needs from Saugeen Summerleaf
Determine high level solution, i.e.
Raspberry PI / Arduino with wired sensor vs. WIFI enabled sensor
Data storage: Local SD card or cloud-based
Research and select sensor
gateway
sensor

## Slide 6: System Design
Hardware Design
  Bluetooth sensors placed inside storage boxes
  Sensor Gateway placed in room with BT connectivity to sensor and WIFI to cloud
Software Design
  Python code to periodically read sensor data via Sensor provide cloud API
  Data stored in MS SQL database on local PC
  Simple dashboard for visualization

## Slide 7: System Design
Wifi router
Storage containers with sensor
Sensor
gateway
Bluetooth
HTTP
HTTP
SensorPush Cloud
Location: Store
Location: Office
Python
Database
Server
Web Server
PC
HTTP
HTTP

## Slide 8: Prototyping - Collect Data In first half of semester
Setup and connect SensorPush sensor and gateway
Create SensorPush account for Cloud API usage
Create python program to:
  authenticate with SensorPush cloud REST API
  fetch sensors linked to account
  periodically fetch data from sensor
  save fetched temperature and humidity data into local MS SQL Server DB

## Slide 9: Prototyping – Visualize Data In second half of semester
Investigate web dashboard solutions
Create simple web application that fetches data from database and visualizes data in a graph
Optional enhancements:
Filter data visualization by sensor, date range etc
Alarm configuration when reaching threshold
Send notification (email) when threshold reached

## Slide 10: Implementation
Fix sensor in storage box
Combine prototyping scripts (fetch data script and store to DB script)
Improve Cloud API authentication so not to hardcode passwords
Create and host web application to visualize data

## Slide 11: Testing and validation
Purchase additional sensors to test collection and visualization of multiple sensors
Train business manager on how to use the solution
Provide instructions and documentation to business

## Slide 12: Deployment and Maintenance
If solution is working good, customer is considering deploying solution in sister store as well.
Setup SQL Server backup and maintenance
No other maintenance should be needed with this solution

## Slide 13: Conclusion
A lot of time was spent finding a sensor that is not wired and supports wifi, either directly or via a gateway.
Was able to use different aspects of what I learned in the past 3 years such as MS SQL Server, Python programming, Web development, protocols such as HTTP (for REST APIs) and of course Project Management.
Enjoyed working on a real project that will actually be used, rather than just a school project.

## Slide 14: Questions